## Slide 1: COSC121: Computer Systems. Managing Memory
Jeremy Bolton, PhD
Assistant Teaching Professor
Constructed using materials:
- Patt and Patel Introduction to Computing Systems (2nd)
- Patterson and Hennessy Computer Organization and Design (4th)
**A special thanks to Eric Roberts and Mary Jane Irwin

## Slide 2: Notes
Read PH.5 and PH.6

## Slide 3: Outline
Memory
  Technology
  Speed
  Schemes for efficiency
    Cache hierarchy
    Virtual Memory
    How to manage and efficiently use cache
      …

## Slide 4: This week … our journey takes us …
I/O system
Processor
Compiler
Operating
System
(Win, Linux)
Application (Browser)
Digital Design
Circuit Design
Instruction Set
Architecture
Datapath & Control
transistors
Memory
Hardware
Software
Assembler
COSC 120: Computer Hardware
COSC 121: Computer Systems
COSC 255: Operating Systems
Drivers

## Slide 5: Virtual Memory
Use main memory as a “cache” for secondary (disk) storage
  Managed jointly by CPU hardware and the operating system (OS)
Programs share main memory
  Each gets a private virtual address space holding its frequently used code and data
  Protected from other programs
CPU and OS translate virtual addresses to physical addresses
  VM “block” is called a page
  VM translation “miss” is called a page fault

## Slide 6: Address Translation
Fixed-size pages (e.g., 4K)

## Slide 7: Page Fault Penalty
On page fault, the page must be fetched from disk
  Takes millions of clock cycles
  Handled by OS code (software is slow)
Try to minimize page fault rate
  Fully associative placement
  Smart replacement algorithms

## Slide 8: Page Tables
Stores placement information
  Array of page table entries, indexed by virtual page number
  Page table register in CPU points to page table in physical memory
If page is present in memory
  PTE stores the physical page number
  Plus other status bits (referenced, dirty, …)
If page is not present
  PTE can refer to location in swap space on disk

## Slide 9: Translation Using a Page Table

## Slide 10: Mapping Pages to Storage

## Slide 11: Replacement and Writes
To reduce page fault rate, prefer least-recently used (LRU) replacement
  Reference bit (aka use bit) in PTE set to 1 on access to page
  Periodically cleared to 0 by OS
  A page with reference bit = 0 has not been used recently
Disk writes take millions of cycles
  Block at once, not individual locations
  Write through is impractical
  Use write-back
  Dirty bit in PTE set when page is written

## Slide 12: Fast Translation Using a TLB
Address translation would appear to require extra memory references
  One to access the PTE
  Then the actual memory access
But access to page tables has good locality
  So use a fast cache of PTEs within the CPU
  Called a Translation Look-aside Buffer (TLB)
  Typical: 16–512 PTEs, 0.5–1 cycle for hit, 10–100 cycles for miss, 0.01%–1% miss rate
  Misses could be handled by hardware or software

## Slide 13: Fast Translation Using a TLB

## Slide 14: TLB Misses
If page is in memory
  Load the PTE from memory and retry
  Could be handled in hardware
    Can get complex for more complicated page table structures
  Or in software
    Raise a special exception, with optimized handler
If page is not in memory (page fault)
  OS handles fetching the page and updating the page table
  Then restart the faulting instruction

## Slide 15: TLB Miss Handler
TLB miss indicates
  Page present, but PTE not in TLB
  Page not preset
Must recognize TLB miss before destination register overwritten
  Raise exception
Handler copies PTE from memory to TLB
  Then restarts instruction
  If page not present, page fault will occur

## Slide 16: Page Fault Handler
Use faulting virtual address to find PTE
Locate page on disk
Choose page to replace
  If dirty, write to disk first
Read page into memory and update page table
Make process runnable again
  Restart from faulting instruction

## Slide 17: TLB and Cache Interaction
If cache tag uses physical address
  Need to translate before cache lookup
Alternative: use virtual address tag
  Complications due to aliasing
    Different virtual addresses for shared physical address

## Slide 18: The Memory Hierarchy
Common principles apply at all levels of the memory hierarchy
  Based on notions of caching
At each level in the hierarchy
  Block placement
  Finding a block
  Replacement on a miss
  Write policy
The BIG Picture

## Slide 19: COSC121: Computer Systems. Cache Coherency (if time)
Jeremy Bolton, PhD
Assistant Teaching Professor
Constructed using materials:
- Patt and Patel Introduction to Computing Systems (2nd)
- Patterson and Hennessy Computer Organization and Design (4th)
**A special thanks to Eric Roberts and Mary Jane Irwin

## Slide 20: FSM Cache Controller
Key characteristics for a simple L1 cache
  Direct mapped
  Write-back using write-allocate
  Block size of 4 32-bit words (so 16B); Cache size of 16KB (so 1024 blocks)
  18-bit tags, 10-bit index, 2-bit block offset, 2-bit byte offset, dirty bit, valid bit, LRU bits (if set associative)
Cache
&
Cache
Controller
1-bit Read/Write
Processor
DDR SDRAM
1-bit Valid
32-bit address
32-bit data
32-bit data
1-bit Ready
1-bit Read/Write
1-bit Valid
32-bit address
128-bit data
128-bit data
1-bit Ready
Notes: A blocking cache so the processor must wait until the cache has finished this request
Memory controller will notify the Cache Controller via the Ready signal when the memory read or write is finished

## Slide 21: Four State Cache Controller
Idle
Compare Tag
If Valid && Hit
Set Valid, Set Tag,
If Write set Dirty
Allocate
Read new block
from memory
Write Back
Write old block
to memory
Cache Hit
Mark Cache Ready
Cache Miss
Old block is
Dirty
Memory Ready
Memory Ready
Memory
Not Ready
Memory
Not Ready
Cache Miss
Old block is
clean
Valid CPU request
Notes: Idle – waits for a Read/Write request from the Processor along with a Valid signal, FSM moves to Compare Tag state
Compare Tag – Checks to see if the request is a hit or a miss. On hit and Valid, returns data to the Processor and moves back to Idle state. On miss, if dirty goes to Write Back state or to Allocate state.
Write Back – Writes the 128-bit block to Memory. When memory write is complete move to the Allocate state.
Allocate – Fetch new block from Memory. Wait in this state until the Memory returns a Ready signal. Then write new block into the Cache and return to the Compare Tag state.

## Slide 22: Cache Coherence in Multicores
In future multicore processors its likely that the cores will share a common physical address space, causing a cache coherence problem
Core 1
Core 2
L1 I$
L1 D$
Unified (shared) L2
L1 I$
L1 D$
Notes: For class handout

## Slide 23: Cache Coherence in Multicores
In future multicore processors its likely that the cores will share a common physical address space, causing a cache coherence problem
Core 1
Core 2
L1 I$
L1 D$
Unified (shared) L2
L1 I$
L1 D$
X = 0
X = 0
X = 0
Read X
Read X
Write 1 to X
X = 1
X = 1
Notes: For lecture
Assumes a write through L1 cache

## Slide 24: A Coherent Memory System
Any read of a data item should return the most recently written value of the data item
  Coherence – defines what values can be returned by a read
    Writes to the same location are serialized (two writes to the same location must be seen in the same order by all cores)
  Consistency – determines when a written value will be returned by a read
To enforce coherence, caches must provide
  Replication of shared data items in multiple cores’ caches
    Replication reduces both latency and contention for a read shared data item
  Migration of shared data items to a core’s local cache
    Migration reduced the latency of the access the data and the bandwidth demand on the shared memory (L2 in our example)
Notes: Supporting migration and replication is critical to performance in accessing shared data.

## Slide 25: Cache Coherence Protocols
Need a hardware protocol to ensure cache coherence the most popular of which is snooping
  The cache controllers monitor (snoop) on the broadcast medium (e.g., bus) with duplicate address tag hardware (so they don’t interfere with core’s access to the cache) to determine if their cache has a copy of a block that is requested
Write invalidate protocol – writes require exclusive access and invalidate all other copies
  Exclusive access ensure that no other readable or writable copies of an item exists
If two processors attempt to write the same data at the same time, one of them wins the race causing the other core’s copy to be invalidated. For the other core to complete, it must obtain a new copy of the data which must now contain the updated value – thus enforcing write serialization
Notes:   Reading from multiple copies is not a problem!! Only writes cause issues. What happens if two processors try to write to the same shared data word in the same clock cycle? The bus arbiter decides which processor gets the bus first (and this will be the processor with the first exclusive access). Then the second processor will get exclusive access. Thus, bus arbitration forces sequential behavior.
  This sequential consistency is the most conservative of the memory consistency models. With it, the result of any execution is the same as if the accesses of each processor were kept in order and the accesses among different processors were interleaved.
Each block needs an additional state bit – owner - which indicates that a block may be shared, but the owning core is responsible for updating any other processors and memory when it changes the block or replaces it.
An alternative to snooping is a directory based cache coherence protocol where the directory keeps the sharing status of blocks of physical memory. They have slightly higher implementation overhead but can reduc traffic between caches and thus scale to larger core counts.

## Slide 26: Handling Writes
Ensuring that all other processors sharing data are informed of writes can be handled two ways:
Write-update (write-broadcast) – writing processor broadcasts new data over the bus, all copies are updated
  All writes go to the bus  higher bus traffic
  Since new values appear in caches sooner, can reduce latency
Write-invalidate – writing processor issues invalidation signal on bus, cache snoops check to see if they have a copy of the data, if so they invalidate their cache block containing the word (this allows multiple readers but only one writer)
  Uses the bus only on the first write  lower bus traffic, so better use of bus bandwidth
Notes: IN HIDE MODE – NEEDED?
All commercial machines use write-invalidate as their standard coherence protocol

## Slide 27: Example of Snooping Invalidation
Core 1
Core 2
L1 I$
L1 D$
Unified (shared) L2
L1 I$
L1 D$
Notes: For class handout

## Slide 28: Example of Snooping Invalidation
When the second miss by Core 2 occurs, Core 1 responds with the value canceling the response from the L2 cache (and also updating the L2 copy)
Core 1
Core 2
L1 I$
L1 D$
Unified (shared) L2
L1 I$
L1 D$
X = 0
X = 0
X = 0
Read X
Read X
Write 1 to X
X = 1
Read X
X = I
X = I
X = 1
X = 1
Notes: For lecture
Snooping bus with write-back L1 cache. Requires an additional state – called owner – which indicates that a block may be shared, but the owning core is responsible for updating any other processors and memory when it changes the block or replaces it

## Slide 29: A Write-Invalidate CC Protocol
Shared
(clean)
Invalid
Modified
(dirty)
write-back caching protocol in black
read (miss)
write (hit or miss)
read (hit or miss)
read (hit) or write (hit or miss)
write (miss)
Notes: For class handout

## Slide 30: A Write-Invalidate CC Protocol
Shared
(clean)
Invalid
Modified
(dirty)
write-back caching protocol in black
read (miss)
write (hit or miss)
read (hit or miss)
read (hit) or write (hit)
write (miss)
send invalidate
receives invalidate
(write by another core
to this block)
write-back due to read (miss) by another core to this block
send invalidate
signals from the core in red
signals from the bus in blue
Notes: For lecture
A read miss causes the cache to acquire the bus and write back the victim block (if it was in the Modified (dirty) state). All the other caches monitor the read miss to see if this block is in their cache. If one has a copy and it is in the Modified state, then the block is written back and its state is changed to Invalid. The read miss is then satisfied by reading from the block memory, and the state of the block is set to Shared.
Read hits do not change the cache state.
A write miss to an Invalid block causes the cache to acquire the bus, read the block, modify the portion of the block being written and changing the block’s state to Modified. A write miss to a Shared block causes the cache to acquire the bus, send an invalidate signal to invalidate any other existing copies in other caches, modify the portion of the block being written and chang the block’s state to Modified.
A write hit to a Modified block causes no action. A write hit to a Shared block causes the cache to acquire the bus, send an invalidate signal to invalidate any other existing copies in other caches, modify the part of the block being written, and change the state to Modified.

## Slide 31: Write-Invalidate CC Examples
  I = invalid (many), S = shared (many), M = modified (only one)
Core 1
A S
Main Mem
A
Core 2
A I
Core 1
A S
Main Mem
A
Core 2
A I
Core 1
A M
Main Mem
A
Core 2
A I
Core 1
A M
Main Mem
A
Core 2
A I
Notes: SKIP THIS – FAR TOO MUCH DETAIL, EARLIER EXAMPLE SUFFICES
For class handout

## Slide 32: Write-Invalidate CC Examples
  I = invalid (many), S = shared (many), M = modified (only one)
1. read miss for A
2. read request for A
3. snoop sees read request for A & lets MM supply A
4. gets A from MM & changes its state to S
1. write miss for A
2. writes A & changes its state to M
1. read miss for A
3. snoop sees read request for A, writes-back A to MM
2. read request for A
4. gets A from MM & changes its state to M
3. C2 sends invalidate for A
4. change A state to I
5. C2 sends invalidate for A
5. change A state to I
1. write miss for A
2. writes A & changes its state to M
3. C2 sends invalidate for A
4. change A state to I
Core 1
A S
Main Mem
A
Core 2
A I
Core 1
A S
Main Mem
A
Core 2
A I
Core 1
A M
Main Mem
A
Core 2
A I
Core 1
A M
Main Mem
A
Core 2
A I
Notes: SKIP THIS – FAR TOO MUCH DETAIL, EARLIER EXAMPLE SUFFICES
For lecture
1st example – supplying A from Core 1 cache would be faster than getting it from MM
2nd and 4th example – assumes a Write allocate cache policy

## Slide 33: Data Miss Rates
Shared data has lower spatial and temporal locality
  Share data misses often dominate cache behavior even though they may only be 10% to 40% of the data accesses
64KB 2-way set associative data cache with 32B blocks
Hennessy & Patterson, Computer Architecture: A Quantitative Approach
Notes: Compulsory misses are all very small and are included in capacity misses. The x axis is core count

## Slide 34: Block Size Effects
Writes to one word in a multi-word block mean that the full block is invalidated
Multi-word blocks can also result in false sharing: when two cores are writing to two different variables that happen to fall in the same cache block
  With write-invalidate false sharing increases cache miss rates
Compilers can help reduce false sharing by allocating highly correlated data to the same cache block
A
B
Core1
Core2
4 word cache block

## Slide 35: Other Coherence Protocols
There are many variations on cache coherence protocols
Another write-invalidate protocol used in the Pentium 4 (and many other processors) is MESI with four states:
  Modified – same
  Exclusive – only one copy of the shared data is allowed to be cached; memory has an up-to-date copy
    Since there is only one copy of the block, write hits don’t need to send invalidate signal
  Shared – multiple copies of the shared data may be cached (i.e., data permitted to be cached with more than one processor); memory has an up-to-date copy
  Invalid – same
Notes: For E and S book states that memory has an up-to-date version so is this not a write-back cache ???

## Slide 36: MESI Cache Coherency Protocol
Processor write
or read hit
Modified
(dirty)
Invalid
(not valid
block)
Shared
(clean)
Processor
write
miss
Processor
shared read
miss
Processor
write
[Send invalidate signal]
[Write back block]
Processor
shared read
Invalidate for this block
Another
processor
has read/write
miss for this
block
[Write back block]
Exclusive
(clean)
Processor
exclusive
read
Processor exclusive
read miss
Processor
exclusive
read
Processor
exclusive
read miss
[Write back block]
Processor
shared
read
Notes: In hide mode – too complicated for this undergraduate class.
If going to include need to cleanup and animate it.

## Slide 37: Appendix
Jeremy Bolton, PhD
Assistant Teaching Professor
Constructed using materials:
- Patt and Patel Introduction to Computing Systems (2nd)
- Patterson and Hennessy Computer Organization and Design (4th)
**A special thanks to Eric Roberts and Mary Jane Irwin