## Slide 1: COSC579: Scene Geometry
Jeremy Bolton, PhD
Assistant Teaching Professor

## Slide 2: Overview
Linear Algebra Review
  Homogeneous vs non-homogeneous representations
  Projections and Transformations
Scene Geometry
The pinhole projection model
  Qualitative properties
  Perspective projection matrix
Cameras with lenses
  Depth of focus
  Field of view
  Lens aberrations

## Slide 3: Scene Geometry, Projection, and Perspective
Readings
  Szeliski 2.1

## Slide 4: Projection
Readings
  Szeliski 2.1

## Slide 5: Dimensionality Reduction (3D to 2D)
Figures © Stephen E. Palmer, 2002
3D world
2D image
What have we lost?
  Angles
  Distances (lengths)
Slide by A. Efros

## Slide 6: Linear Algebra and Projections
Before we dive into camera geometry, lets introduce some notation and review linear algebra.
2-D points will be used to represent pixel coordinates: points in a (image) plane. (non-homogeneous)

## Slide 7: Homogeneous and Non-homogeneous Vectors
2-D points can be represented by a vector and a weight.
  Homogeneous
  P2 is the 2-d projective space

## Slide 8: Why Homogeneous Coordinates?
Homogeneous representation permits linear matrix operations for transformations used in Computer Vision
How? add one more coordinate:
homogeneous image
coordinates
homogeneous scene
coordinates
Converting from homogeneous coordinates

## Slide 9: Lines
2-D Lines can also be represented using homogeneous coordinates
Corresponding line equation
It is common to normalize the line equation vector
Observe: in this formulation is the unit normal vector perpendicular to the line and d is its distance to the origin

## Slide 10: Lines
Computing the intersection of 2 lines using homogeneous coordinates
Computing the line joining two points using homogeneous coordinates

## Slide 11: 3-D
Similar representations exist to model 3-D points: points in a scene.
3-D planes specification using homogeneous coordinates
Equation of plane
Normalized

## Slide 12: Lines in 3-D
Not as easy to represent
One method: model line segment r as convex combination of two points on the line.
  Assume p and q are points on the line.
Homogeneous coordinates

## Slide 13: Lines in 3-D
More generally, we can represent a line in 3-D using a point and a gradient

## Slide 14: 2D Planar Transformations

## Slide 15: Translations
Here the augmented vector is used to account for translation t
Simply a shift

## Slide 16: Euclidean Transformations

## Slide 17: Scaled Rotations

## Slide 18: Affine

## Slide 19: Projective Transformation (Homography)

## Slide 20: Properties of Transformations

## Slide 21: 3D transformations

## Slide 22: 3D Euclidean Transformation

## Slide 23: 3D similarity transformation

## Slide 24: 3D Affine Transformation

## Slide 25: Projective Transformation

## Slide 26: 3D Rotations
Sequential Rotations Approach (Euler Angle).
  Perform 3 sequential rotations around 3 cardinal axes.
  Cons
    Result depends on order of rotations.
    Not always practical
Axis / Angle Approach
  Rotation can be determined by 1 rotation axis and 1 angle

## Slide 27: 3D Axis/Angle Rotation
Constructing the rotation matrix R, given and

## Slide 28: Projecting from 3D to 2D
Projections
  Orthographic and scaled orthographic (weak perspective) projection
  Para-perspective projection
  Perspective projection
These projects are used often during image formation.

## Slide 29: Modeling projection
The coordinate system
  We will use the pin-hole model as an approximation
  Put the optical center (Center Of Projection) at the origin
  Put the image plane (Projection Plane) in front of the COP
    Why?
  The camera looks down the negative z axis
    we need this if we want right-handed-coordinates
Notes: This way the image is right-side-up

## Slide 30: Orthographic projection
Special case of perspective projection
  Distance from the COP to the PP is infinite (ignore z-axis)
  Good approximation for telephoto optics
  Also called “parallel projection”: (x, y, z) → (x, y)
  What’s the projection matrix?
Image
World

## Slide 31: Variants of orthographic projection
Scaled orthographic
  Also called “weak perspective”
Affine projection
  Also called “para-perspective”

## Slide 32: Modeling projection
Projection equations
  Compute intersection with PP of ray from (x,y,z) to COP
  Derived using similar triangles (Try this at Home!)
  We get the projection by throwing out the last coordinate:

## Slide 33: Perspective Projection
Projection is a matrix multiply using homogeneous coordinates:
divide by third coordinate
This is known as perspective projection
  The matrix is the projection matrix
  Can also formulate as a 4x4
divide by fourth coordinate

## Slide 34: Projection Review
Reviewed
  Linear algebra and notation
  Projections
Projections are used to model image formation and analysis
To see where projections fit in, lets investigate camera models

## Slide 35: Camera Models
Jeremy Bolton, PhD
Assistant Teaching Professor

## Slide 36: Image formation
Let’s design a camera
  Idea 1: put a piece of film in front of an object
  Do we get a reasonable image?
Notes: Light comes from everywhere. Without of means of focus, everything is a blur

## Slide 37: Pinhole camera
Add a barrier to block off most of the rays
  This reduces blurring
  The opening known as the aperture
  How does this transform the image?
Notes: It gets inverted

## Slide 38: Camera Obscura: Pinhole model
The first camera
  Known to Aristotle
  How does the aperture size affect the image?
Pinhole model:
  Captures pencil of rays – all rays through a single point
  The point is called Center of Projection (focal point)
  The image is formed on the Image Plane

## Slide 39: Shrinking the aperture
Why not make the aperture as small as possible?
  Less light gets through
  Diffraction effects...

## Slide 40: Shrinking the aperture

## Slide 41: The eye
The human eye is a camera
  Iris - colored annulus with radial muscles
  Pupil - the hole (aperture) whose size is controlled by the iris
  What’s the “film”?
    photoreceptor cells (rods and cones) in the retina
Notes: Note that the retina is curved

## Slide 42: Different Camera (and Projection) Models
Pinhole Camera (Central Perspective)
  Weak Perspective Projection
  Orthographic Projection
Thin Lens Camera

## Slide 43: Pinhole Camera Model
A simplistic yet convenient projective model.
  Also known as central perspective model.
  Most cameras have lenses however, this model often provides an acceptable approximation to an imaging system in many applications.
  Image coordinates can be computed using similar triangles
  Convenient virtual image plane.

## Slide 44: Pinhole: Modeling projection
The coordinate system
  Assumption: use the pinhole model as a reasonable approximation
  Put the optical center (O) at the origin
  Put the image plane (Π’) in front of O
Source: J. Ponce, S. Seitz
x
y
z
d
Notes: This way the image is right-side-up

## Slide 45: Pinhole: Modeling projection
Projection equations
  Compute intersection with Π’ of ray from P = (x,y,z) to O
  Derived using similar triangles
Source: J. Ponce, S. Seitz
  We get the projection by “throwing” out the last coordinate:
x
y
z
d

## Slide 46: Weak Perspective (Scaled Orthography)
Assume points are projected toward pinhole and intersect an image plane “before” intersecting origin.
  Fronto-Parallel Plane. A virtual plane whose distance from the origin along the z axis is variable: Z’
  Plane Equation Z = Z’ , that is, assume z is constant

## Slide 47: Weak Perspective (Scaled Orthography)
Substituting into pinhole equation, we see that image coordinates can be estimated from a magnification factor m.
Thus image coordinates are estimated by using factor m

## Slide 48: Orthographic Perspective
Assume magnification is 1, that is d = Z’
  Interpretation: Planar scene at constant distance which is always known
  Often unrealistic assumption unless points are very very far away.
  Simply ignore Z component

## Slide 49: Lens Models
Lens model
  Most cameras have lenses
  Permits larger aperture while refractive properties focus the light
Thin lens model
  Lens is flat (no length along optical axis)
Thick lens or spherical lens models (ignored)
  Assumes lens has volume

## Slide 50: Adding a lens
A lens focuses light onto the film
  Rays passing through the center are not deviated
Slide by Steve Seitz

## Slide 51: Adding a lens
A lens focuses light onto the film
  There is a specific distance at which objects are “in focus”
    other points project to a “circle of confusion” in the image
  Changing the shape of the lens changes this distance
“circle of
confusion” resulting in blur

## Slide 52: Lenses
A lens focuses parallel rays onto a single focal point
  focal point at a distance f beyond the plane of the lens
    f is a function of the shape and index of refraction of the lens
  Aperture of diameter D restricts the range of rays
    aperture may be on either side of the lens
  Lenses are typically spherical (easier to produce)
focal point
F
optical center
(Center Of Projection)

## Slide 53: Thin lenses
Thin lens equation:
  Any object point satisfying this equation is in focus
  What is the shape of the focus region?
  How can we change the focus region?
  Thin lens applet: http://www.phy.ntnu.edu.tw/java/Lens/lens_e.html (by Fu-Kwun Hwang )

## Slide 54: Pinhole vs Thin Lens
Observe: Similar to pinhole model when d = z. Only admitting ray of light passing through O. However, using a lens, images will only be in focus if z is appropriately chosen using thin lens equation.
Thus we can compute image coordinates via pinhole model using d = z.
Note: In many camera models the assumption that f = z = d is made. This simplifies the geometry, and is analogous to assuming the camera is focused at inf. In general, the image will not be in focus with this assumption.

## Slide 55: Normalized Image Plane
Choosing a normalized image plane can be useful in many applications.
  Although the actual sensor is located at some distance d from optical center, we can choose a similar (up to a scale) image plane d = 1

## Slide 56: Projections based on Models
We can derive projection matrices based on the camera models
These projection matrices include factors intrinsic to the model and necessary to compute image coordinates
  Some may be known, some are not

## Slide 57: Central Perspective (standard pinhole)
Recall (by similar triangles):
Or Similarly …

## Slide 58: Adding Weak Perspective
Recall:
Instrinsics
Weak
Perspective Projection
Notes: These two matrices can be easily collapsed into one

## Slide 59: Intrinsic Matrix
Transformation Matrix called Intrinsic Matrix as it includes some factors intrinsic to the camera
  distance to sensor
  translation to image center.
  (image coordinates often assume (0,0) is lower corner of image)
  skew factor: sensor axes are not orthogonal, …

## Slide 60: Adding factors for shift and skew
Skew can be due to manufacturing error
Shift may be desired as often, image coordinates begin in lower left corner of image (not where optical axes intersects)
Instrinsics
Weak
Perspective Projection

## Slide 61: Adding Extrinsics
Previous models assume coordinates of camera and scene are the same.
If this is not true, we can map coordinate systems using extrinsic parameters which define the orientation of the camera relative to the scene.
“The World”
Camera
x
y
z
v
w
u
o
COP
Two important coordinate systems:
1. World coordinate system
2. Camera coordinate system

## Slide 62: Camera parameters
To project a point (x,y,z) in world coordinates into a camera
First transform (x,y,z) into camera coordinates
Need to know
  Camera position (in world coordinates)
  Camera orientation (in world coordinates)

## Slide 63: Perspective Projection Matrix
divide by the third coordinate
Projection is a matrix multiplication using homogeneous coordinates:
In practice: lots of coordinate transformations…
World to camera coord. trans. matrix (4x4)
Perspective projection matrix (3x4)
Camera to pixel coord. trans. matrix (3x3)
=
2D
point (3x1)
3D point (4x1)
Observe: We can solve for image coordinates in terms of real-world coordinates and transformation parameters

## Slide 64: Perspective projection (Intrinsics)
(intrinsics)
in general,
: aspect ratio (1 unless pixels are not square)
: skew (0 unless pixels are shaped like rhombi/parallelograms)
: principal point ((0,0) unless optical axis doesn’t intersect projection plane at origin)
(upper triangular matrix)
(converts from 3D rays in camera coordinate system to pixel coordinates)

## Slide 65: Projection matrix (Extrinsics)
0
=
(in homogeneous image coordinates)

## Slide 66: Extrinsics
How do we get the camera to “canonical form”?
  (Center of projection at the origin, x-axis points right, y-axis points up, z-axis points backwards)
0
Step 1: Translate by -c

## Slide 67: Extrinsics
How do we get the camera to “canonical form”?
  (Center of projection at the origin, x-axis points right, y-axis points up, z-axis points backwards)
0
Step 1: Translate by -c
How do we represent translation as a matrix multiplication?

## Slide 68: Extrinsics
How do we get the camera to “canonical form”?
  (Center of projection at the origin, x-axis points right, y-axis points up, z-axis points backwards)
0
Step 1: Translate by -c
Step 2: Rotate by R
3x3 rotation matrix

## Slide 69: Extrinsics
How do we get the camera to “canonical form”?
  (Center of projection at the origin, x-axis points right, y-axis points up, z-axis points backwards)
0
Step 1: Translate by -c
Step 2: Rotate by R

## Slide 70: Camera parameters
Projection equation
  The projection matrix models the cumulative effect of all parameters
  Useful to decompose into a series of operations
Intrinsics
rotation
translation
A camera is described by several parameters
  Translation t of the optical center from the origin of world coords
  Rotation R of the image plane
  focal length f = d, principle point (x’c, y’c),
  blue parameters are called “extrinsics,” red are “intrinsics”
  Note: The definitions of these parameters are not completely standardized
Extrinsics
Weak
Perspective
This assumption is common though may be unrealistic

## Slide 71: Camera Models
Scene geometry consists of internal and external parameters
Observed light is focused onto an image plane
The image is then captured (Image Acquisition)
But first we will review radiometry: physics of LIGHT and COLOR

## Slide 72: Appendix
Jeremy Bolton, PhD
Assistant Teaching Professor

## Slide 73: Pinhole Camera Model
Using Princes Notation.

## Slide 74: Geometric interpretation of homogeneous coordinates

## Slide 75: Normalized Camera
By similar triangles:

## Slide 76: Focal length parameters

## Slide 77: Focal length parameters
Can model both
  the effect of the distance to the focal plane
  the density of the receptors
with a single focal length parameter f = d = f
To be overly cumbersome note: In practice, the receptors may not be square:
So use different focal length parameter for x and y dims

## Slide 78: Offset parameters
Current model assumes that pixel (0,0) is where the principal ray strikes the image plane (i.e. the center)
Model offset to center

## Slide 79: Skew parameter
Finally, add skew parameter
Accounts for image plane being not exactly perpendicular to the principal ray

## Slide 80: Pinhole camera in homogeneous coordinates
Camera model:
In homogeneous coordinates:
(linear!)

## Slide 81: Pinhole camera in homogeneous coordinates
Writing out these three equations
Eliminate l to retrieve original equations

## Slide 82: Position and orientation of camera
Position w=(u,v,w)T of point in the world is generally not expressed in the frame of reference of the camera.
Transform using 3D transformation
or
Point in frame of reference of camera
Point in frame of reference of world

## Slide 83: Complete pinhole camera model
Intrinsic parameters (stored as intrinsic matrix)
Extrinsic parameters